EXPERIMENTAL EVALUATION OF NONLINEAR INDICES FOR ULTRASOUND TRANSDUCER CHARACTERIZATIONS

BY

TIMOTHY ALLEN BIGELOW

B.S., Colorado State University, 1998

THESIS

Submitted in partial fulfillment of the requirements

for the degree of Master of Science in Electrical Engineering

in the Graduate College of the

University of Illinois at Urbana-Champaign, 2001

### Urbana, Illinois

# ACKNOWLEDGMENTS

## First of all, I would like to thank my adviser, Dr. William O’Brien for his help on this work. I would also like to thank Dr. Andrew Webb for the use of his lab and network analyzer and Dr. Narendra Ahuja for guidance when I first came to the University of Illinois at Urbana-Champaign.  I would also like to recognize my coworkers in the Bioacoustics Research Laboratory because of help they provided during the investigation.  Last of all, I want to reference Exodus 15:2 and 1 Corinthians 3:11-15.

### TABLE OF CONTENTS

CHAPTER                                                                                                                   PAGE

#### INTRODUCTION TO THE NONLINEAR INDEX PROBLEM ..……...…..……… 1

  - Background: Extrapolation in Ideal Linear Case ….…………....………..……… 1

  - Motivation: Problems Introduced by Acoustical Nonlinear Effects …..…..…….. 6

  - Approach and Summary of Results ……..………………………………….…… 7

#### THEORETICAL ANALYSIS OF ASYMMETRIC DISTORTION …………….…. 9

  - The Modified Ostrovskii/Sutin Method ……..……………………….….…...…. 9

  - Some Inherent Problems with the Ostrovskii/Sutin Method …………………... 13

  - Insights Provided by the Ostrovskii/Sutin Method ………………………...……17

#### THEORETICAL ANALYSIS OF NONLINEAR ABSORPTION …………..….… 21

#### Acoustical Saturation for Plane Waves ……………………………………….. 21

#### Nonlinear Absorption for a Focused Sound Source …………………………... 24

#### THEORETICAL ANALYSIS OF PROPOSED INDICES ……………...………… 26

  - Absolute Indicators of Nonlinearity …………………………………….…...…. 26

    - Asymmetric ratio ………………………..………………………..…...... 27

    - Ostrovskii/Sutin’s propagation parameter s ………….……………...... 28

    - Bacon’s propagation parameter m ……….……………………....….… 30

    - Field sigma z …………………………..….…………...……….......…. 35

    - Second harmonic ratio ……………………………..………………...… 35

    - Absolute spectral index ………………………..……………………..… 37

  - Relative Indicators of Nonlinearity .……………………………………………. 38

    - Relative spectral index ………………………………………………..... 39

    - Relative focal pressure ……………………………………………….… 39

#### ANALYSIS OF EXTRAPOLATION VOLTAGES ……………………….……..... 41

  - Extrapolation Factor Candidates ……………………………….…….….…...… 41

  - Experimental Evaluation of Candidates …...……………..………………...…... 47

  - Setting the Confidence Measure for each Data Set …….…………………....…. 53

- EXPERIMENTAL PROCEDURE ……………………………………………........ 54

  - Overview of Experimental System …………………………………………….. 54

  - Analysis of Excitation System ……………………….………………………… 55

  - Data Acquisition …………………………………………………...………...… 61

- EXPERIMENTAL EVALUATION OF PROPOSED INDICES …...……..…….… 66

  - Calculation of Indices at Each Applied Voltage …………….………………..... 66

  - Determination of Threshold Values of Indices …………...………..………..…. 81

  - Evaluation of the Different Indices …………………………………………….. 89

#### CONCLUSIONS AND FUTURE WORK ……………………………………...…. 93

APPENDIX A: POISSON’S THEOREM …..……...……………………………… 95

APPENDIX B: THE KLM MODEL ….....………………………………………… 99

APPENDIX C: THE RLC CIRCUIT MODEL FOR A PIEZOELECTRIC

TRANSDUCER …................................................................…….. 104

## APPENDIX D: COMPARISON OF THE RLC CIRCUIT MODEL TO THE

KLM MODEL …....................................................................…... 106

APPENDIX E: MATLAB CODE TO DETERMINE THE RLC VALUES FOR

THE CIRCUIT MODEL ……...…………………………………... 116

APPENDIX F: MATLAB CODE USED TO DETERMINE EXTRAPOLATION

FACTOR …............................................................................…….. 119

## APPENDIX G: MATLAB CODE USED TO EVALUATE NONLINEAR

## INDICATORS ……................................................................….... 129

REFERENCES …………………...……………………………………………….. 149

### LIST OF TABLES

Table                                                                                                                               Page

5.1: Frequency ranges used to determine RLC parameters ….……...………...……...… 45

5.2: RLC parameters determined for each transducer ……………………………….…. 47

5.3: Linearity of the “close” pressure waveforms quantified in terms of the mean extrapolation error using pr as the extrapolation factor …………………………… 50

5.4: Evaluation of extrapolation factors for pc quantified in terms of the mean extrapolation error determined from the close pressure waveforms ……………… 51

5.5: Evaluation of extrapolation factors for pr quantified in terms of the mean extrapolation error determined from the close pressure waveforms ……………… 51

5.6: Evaluation of extrapolation factors for pavg quantified in terms of the mean extrapolation error determined from the close pressure waveforms ……………… 51

5.7: Scores used to select the best extrapolation factor ………………………………... 53

6.1: Values used for the shunt inductance ……………………………………………... 60

6.2: Step sizes used to find the location of the focus for each transducer ……………... 62

6.3: “Close” locations for each transducer …………………………………………….. 63

### LIST OF FIGURES

Figure                                                                                                                             Page

1.1: The KLM model of a piezoelectric transducer ……………....……...……….......…. 2

1.2: Diagram of a typical focused transducer …………………………………………..... 4

1.3: Plot illustrating asymmetric distortion for a focused source ……………………...… 6

2.1: Diagram illustrating different regions of propagation used in the Ostrovskii/Sutin Method …………………………………………………………………………….... 9

2.2: Results demonstrating pulse asymmetry near the focal region ……………………. 19

3.1: Plots illustrating shock formation for a propagating plane wave ………………….. 23

4.1: Typical frequency spectrum at the focus of a spherically focused transducer under two different drive conditions ………………………………………………...…… 36

5.1: Equivalent RLC circuit model for a piezoelectric transducer …………………...… 42

5.2: Comparison of output simulation results from the RLC circuit model and the KLM model under two different load conditions ………………………………………... 43

5.3: Example measured admittance curve for one of the transducers ………………….. 45

5.4: Typical errors in pc using pr as an extrapolation factor ….………………………… 49

6.1: Diagram of experimental setup ……………………………………………………. 55

6.2: Pulses generated with matched load and transducer connected to the RAM5000 … 57

6.3: Voltage pulses after implementation of restoration procedures …………………… 60

6.4: Diagram illustrating location of “close” pressure measurement ………………...… 64

7.1: First six indicators for a 2.8072 MHz, f/# of 1, 1.905 cm diameter transducer

excited by a “positive going” “three cycle” pulse. (a) Asymmetric ratio Pasym

(b) s from Pasym (c) s from pr (d) m (e) z (f) Second harmonic ratio HII .…….... 67

7.2: Second six indicators for a 2.8072 MHz, f/# of 1, 1.905 cm diameter transducer

excited by a “positive going” “three cycle” pulse. (a) si from 1.51 (b) si from 21

(c) rsi (d)Pce  (e)Pre  (f)Pae .…..................................…………………………..… 68

7.3: First six indicators for a 2.9983 MHz, f/# of 1, 5.08 cm diameter transducer

excited by a “positive going” “three cycle” pulse. (a) Asymmetric ratio Pasym

(b) s from Pasym (c) s from pr (d) m (e) z (f) Second harmonic ratio HII ........… 69

7.4: Second six indicators for a 2.9983 MHz, f/# of 1, 5.08 cm diameter transducer

excited by a “positive going” “three cycle” pulse. (a) si from 1.51 (b) si from 21

(c) rsi (d)Pce  (e)Pre  (f)Pae .…....…………...............................…………..…...… 70

7.5: First six indicators for a 5.4906 MHz, f/# of 1, 1.905 cm diameter transducer

excited by a “positive going” “one cycle” pulse. (a) Asymmetric ratio Pasym

(b) s from Pasym (c) s from pr (d) m (e) z (f) Second harmonic ratio HII .........… 71

7.6: Second six indicators for a 5.4906 MHz, f/# of 1, 1.905 cm diameter transducer

excited by a “positive going” “one cycle” pulse. (a) si from 1.51 (b) si from 21

(c) rsi (d)Pce  (e)Pre  (f)Pae .…...…............................……..….………...……...… 72

7.7: First six indicators for a 5.4906 MHz, f/# of 1, 1.905 cm diameter transducer

excited by a “positive going” “three cycle” pulse. (a) Asymmetric ratio Pasym

(b) s from Pasym (c) s from pr (d) m (e) z (f) Second harmonic ratio HII .…....… 73

7.8: Second six indicators for a 5.4906 MHz, f/# of 1, 1.905 cm diameter transducer

excited by a “positive going” “three cycle” pulse. (a) si from 1.51 (b) si from 21

(c) rsi (d)Pce  (e)Pre  (f)Pae …..................................………..…..…...………....… 74

7.9: First six indicators for a 5.4906 MHz, f/# of 1, 1.905 cm diameter transducer

excited by a “negative going” “three cycle” pulse. (a) Asymmetric ratio Pasym

(b) s from Pasym (c) s from pr (d) m (e) z (f) Second harmonic ratio HII …....… 75

7.10: Second six indicators for a 5.4906 MHz, f/# of 1, 1.905 cm diameter transducer

excited by a “negative going” “three cycle” pulse. (a) si from 1.51 (b) si from 21

(c) rsi (d)Pce  (e)Pre  (f)Pae …....................................………..…..………..…...… 76

7.11: First six indicators for a 5.3574 MHz, f/# of 2, 1.905 cm diameter transducer excited by a “positive going” “three cycle” pulse. (a) Asymmetric ratio Pasym

(b) s from Pasym (c) s from pr (d) m (e) z (f) Second harmonic ratio HII .…....… 77

7.12: Second six indicators for a 5.3574 MHz, f/# of 2, 1.905 cm diameter transducer

excited by a “positive going” “three cycle” pulse. (a) si from 1.51 (b) si from 21

(c) rsi (d)Pce  (e)Pre  (f)Pae .…..................................………..….........………...… 78

7.13: First 6 indicators for a 8.1517 MHz, f/# of 1, 1.905 cm diameter transducer

excited by a “positive going” “three cycle” pulse. (a) Asymmetric ratio Pasym

(b) s from Pasym (c) s from pr (d) m (e) z (f) Second harmonic ratio HII .........… 79

7.14: Second six indicators for a 8.1517 MHz, f/# of 1, 1.905 cm diameter transducer

excited by a “positive going” “three cycle” pulse. (a) si from 1.51 (b) si from 21

(c) rsi (d)Pce  (e)Pre  (f)Pae .…...................................………..…..…..………...… 80

7.15: Threshold values for the asymmetric ratio …………………………….…………. 84

7.16: Threshold values for s from pr ……………………………………….…………. 85

7.17: Threshold values for s from Pasym ………………………………….…...………. 85

7.18: Threshold values for m …………………………………………….……………. 86

7.19: Threshold values for z …………….……………………………….……………. 86

7.20: Threshold values for the second harmonic ratio …………………….…………… 87

7.21: Threshold values for si from 1.51 ………………………………….………….... 87

7.22: Threshold values for si from 21 ………………………………...……….…….... 88

7.23: Threshold values for rsi ………………………………………………….………. 88

7.24: Threshold values for the relative focal pressure ………………………….……… 89

7.25: Direct comparison of pressures at the focus. (a) ~5.5 MHz f/#1 transducer

(b) ~5.5 MHz f/#2 transducer (c) ~8 MHz f/#1 transducer .….………….……….. 90

B.1: The KLM model of the piezoelectric transducer ..................................................... 99

C.1: The RLC circuit model for a piezoelectric transducer ........................................... 104

D.1: Input admittance for the KLM model and the RLC circuit model ......................... 107

D.2: Transfer function for the KLM model and the RLC circuit model ........................ 109